## Slide 1: Reinforcement Learning for Emergency Space-Air-Ground Connectivity: Qusin, Nablus
From a GitHub repository to a reproducible, honest evaluation
Mohammed Yadak | ID 12217817 | October 2026

## Slide 2: The problem: what if the ground network is down?
Six villages around Qusin (west of Nablus) lose service in an emergency
Fall-back: HAPS at 20 km as flying base stations, backed by LEO satellites
Question: how to assign users to HAPS and set power so nobody is left out?
Goal: a problem from our own surroundings, solved with an open-source tool
6
villages, about 16,500 people (2017 census)
4 + 3
HAPS + LEO satellites in the fall-back network

## Slide 3: The tool: a Q-learning SAGIN toolkit (GitHub topic: sagin)
Question | Answer
Why | Correct, reproducible rewrite of an old MATLAB project; teaching and baseline reference (no novelty claim)
What | Python + NumPy; independent tabular Q-learners for user association and transmit power; 3 baselines
Where | Rural and emergency coverage studies, teaching; not a production network planner
When | Quick, transparent experiments (seconds to minutes); baseline for new methods
How | git clone, pip install, python tests.py, python experiment.py
Why this repo: 7 stars, runs on a laptop, ships tests and baselines (the only other repo in the topic needs an LLM API).

## Slide 4: Running the toolkit on my own laptop
python tests.py: 5 sanity tests pass. python experiment.py --quick: Q-learning is +21.6% over the best baseline.

## Slide 5: Scenario: real villages, population-weighted users
Village | Population (2017)
Qusin | 2,251
Deir Sharaf | 2,949
Beit Iba | 4,079
Sarra | 3,384
Zawata | 2,537
Beit Wazan | 1,312
Users placed around villages in proportion to population
30 (moderate) and 45 (busy) representative users
Metrics: outage (< 1 Mbit/s), worst-5% rate, transmit power, blocked users
End-to-end rate = min(access rate, backhaul share)
Coordinates and populations: public village pages citing PCBS 2017.

## Slide 6: A red flag: the first result looked great
Q-learning outage: 14% vs 51% for naive baselines
But the control 'all users on one HAPS' scored 10%
Q-learning had switched off most HAPS (1.5 of 4 active)
Cause: unrealistic radio model; interference swamps the signal
Lesson 1
Always run the simplest possible control before believing a gain.

## Slide 7: The fix: a more realistic radio model
Spot beams
Interference depends on beam angle (35 dBi, 25 dB side-lobe cap)
Frequency reuse
Band split into sub-bands; neighbouring HAPS use different ones
Capacity limit
12 users per HAPS; extra users are blocked
Directional backhaul
Each HAPS points a dish at its LEO; other LEOs are attenuated
A 20 dBi beam covers the whole area; a 35 dBi beam separates users 1-2 km apart.

## Slide 8: Fair baselines changed the conclusion
GreedyLB
Capacity-aware association: strongest users first, best HAPS with room
GreedyLB+LEO
Also balances HAPS across satellites (all HAPS tended to pick the same one)
minP
Smallest common power that keeps outage at 1% or less
SingleHAPS
Control: all users on the best HAPS
21 of 21 outage users were limited by the satellite backhaul
30 topologies per load
Paired differences with 95% bootstrap CIs

## Slide 9: Results: 30 and 45 users, 30 random topologies each
Error bars: standard error over 30 topologies. 3 LEO, 4 HAPS, 35 dBi beams, 2 sub-bands.

## Slide 10: My own run reproduces the article's numbers
python sagin_v2.py: 10 topologies, 20,000 episodes
python paired_stats.py: 30 topologies, 95% bootstrap CIs
Paired results match Table 8 and sweeps match Table 9 of the article

## Slide 11: What the numbers say
-6.4 pp
outage vs best uniform baseline at 45 users (CI -10.5 to -2.2); about 20 W less power
+10.3 pp
outage vs GreedyLB at 45 users: 10.7% vs 0.4%
30 vs 7-15 W
Q-learning vs minP total transmit power
Q-learning clearly beats naive strategies, but not capacity-aware heuristics on outage
Beam gain dominates: at 20 dBi every method has 20-31% outage; at 35 dBi sensible methods are at a few percent
Q-learning is best only when beams are weak (20 dBi)

## Slide 12: Lessons and takeaways
Hardware first
Antenna directivity changes outage far more than the algorithm
Respect capacity, balance the backhaul
The largest avoidable losses come from overloaded HAPS and a single shared satellite
Controls and strong baselines
They turned a flattering plot into evidence
Limits
Simulation with assumed parameters; no claim about real infrastructure
Full tutorial article and code: every step reproducible on a laptop, no GPU.